## Slide 1: MINOR – ROBOTICS AND ARTIFICIAL INTELLIGENCE
COURSE – INTRODUCTION TO ROBOTICS (ME 201M)
MODULE 1
Dr. B. Sandeep Reddy
Assistant Professor, Mechanical Engineering, IIT Guwahati.
Email: bsandeepr@iitg.ac.in

## Slide 2: OVERVIEW OF MINOR PROGRAM
I – MECHANICS
II – SENSING (PERCEPTION)
III – CONTROL
IV – INTELLIGENCE (COGNITION)
INTRODUCTION TO ROBOTICS
(SEM III)
Fundamentals of Artificial
Intelligence(SEM VI)
MECHATRONICS
(SEM IV)
ROBOTIC VISION AND CONTROL (SEM V)
THIS SEMESTER

## Slide 3
MidSem-20 %
End-Sem-30 %
Assignments–30%
Quizzes–20%
GRADING SCHEME

## Slide 4
MODULE 1 (~11 Lectures)
Links and Joints, DOF
Spatial Descriptions – Position and Orientation, Homogeneous Transformations
Different Methods of describing orientation of a rigid body
DH Parameters
Actuation, Transmission and Sensors
MODULE 2 (~12 Lectures)
Serial Robots – Forward and Inverse Kinematics
Velocity and Static analysis of manipulators
Mechanism Design
MODULE 3 (~16 Lectures)
Trajectory planning
Dynamics of robots
MODULE 4 (~ 6 Lectures)
Parallel robots
ROUGH OUTLINE OF THE COURSE

## Slide 5: TEXTBOOKS
Fu. K.S., Gonzalez R.C. and Lee C.S.G., Robotics: Control, Sensing, Vision and Intelligence, Tata McGraw Hill, 2008.
Ghosal A. Robotics: Fundamental Concepts and Analysis, Oxford University Press, 2006.
Craig J.J., Introduction to Robotics – Mechanics and Control, Pearson Prentice Hall, 2005.
Saha. S.K., Introduction to Robotics, McGraw Hill Education (India) Private Limited, 2014.
Spong M.W., Hutchinson S. and Vidyasagar M., Robot Modeling and Control, John Wiley Sons & Inc., 2005.

## Slide 6: OVERVIEW OF KINEMATICS
MODULE 1 – LECTURE 1
OVERVIEW OF KINEMATICS

## Slide 7
WHAT IS A MACHINE ??
A DEVICE FOR TRANSFERRING AND TRANSFORMING MOTION AND FORCE FROM A SOURCE TO THE LOAD
Motion needs to be transformed as it is being transferred from the source to the load
Type of Transformation needed – decided by available input motion and desired output motion
AVAILABLE INPUT MOTION | DESIRED OUTPUT MOTION
Continuous Rotation | Rectilinear Motion
Rectilinear Motion | Continuous Rotation
Continuous Rotation | To and Fro Oscillation
To and Fro Oscillation | Continuous Rotation
Continuous Rotation (Different Speed) | Continuous Rotation (Different Speed)
Continuous Rotation | Angular Oscillation
OVERVIEW OF KINEMATICS OF MACHINES
OVERVIEW OF KINEMATICS

## Slide 8
LATHE
Input motion is available at shaft of driving motor
This motion has to be transferred to two different locations, (i) headstock, to provide motion to the job (ii) tool post, to provide motion to the cutting tool
WHAT KIND OF TRANSFORMATION IS TAKING PLACE HERE ??
The job has to rotate continuously. So, the head stock has to be rotated at different speed than for the input motor, depending on the size of the job, whereas the tool post has to move along a straight line starting from the same input motion.
Thus, we need to have different kinds of devices to transfer and transform from the input to the output.
OVERVIEW OF KINEMATICS

## Slide 9
KINEMATICS
deals with geometric constraint of relative motion, without any reference to the cause of the motion
Input motion is linear – provided by hydraulic actuator and has to be transformed into rotary motion of dumping bin.
linear motion at the hydraulic actuator from the input side is transferred to the bin and is also transformed into the rotary motion
Various components undergo little deformation – can be assumed as rigid
Within paradigm of rigid body, relative motion between various components can be studied from the view point of geometric constraints without any reference to force
WHAT IS KINEMATICS ??
OVERVIEW OF KINEMATICS

## Slide 10
Can be contrasted with a “structure” - structure is also a combination of resistant (rigid) bodies connected by joints, but the purpose of a structure (such as a truss) is not to do work or to transform motion, but to be rigid.
 | Machine | Mechanism
Predominant Idea | force, torque, work, and power | achieving a desired motion
MECHANISM
combination of interconnected rigid bodies capable of relative motion
For the study of kinematics, a machine may be referred to as a mechanism
During the study of kinematics that is of a mechanism, the idea of motion or relative motion predominates and the idea of force takes a back seat.
“Structure” is to statics as “mechanism” is to kinematics as “machine” is to kinetics
OVERVIEW OF KINEMATICS

## Slide 11
KINEMATICS
deals with only geometric aspects of motion without any consideration of force
MECHANISM
combination of interconnected rigid bodies capable of relative motion
The continuous rotation of the drive motor is converted into to and fro oscillation of the wiper blade
Power available at the motor shaft is used to overcome the friction force between the blade and the wind screen.
However, the designer is primarily interested to ensure a proper range of oscillation of the wiper blade, to generate the desired field of wiping.
Hence, it is not called a wiper machine, but a wiper mechanism
OVERVIEW OF KINEMATICS

## Slide 12
How Mechanisms behave depends upon the interconnection amongst members of the mechanism
These Interconnections are called kinematic pairs
What are the various types of kinematic pairs and what kind of relative motion do they permit ?
Number of coordinates needed to describe relative motion permitted in a kinematic pair
Degree of Freedom (DOF)
The coordinates that are used to describe this relative movement are called pair variables
Kinematic Pair
Unconstrained Rigid Body – 6 DOF
one or more of the 6 DOF are curtailed and only a few are retained
Rigid Body is connected to another rigid body
OVERVIEW OF KINEMATICS

## Slide 13: KINEMATIC PAIR
LOWER PAIR
HIGHER PAIR
WRAPPING PAIR
Bodies connected have area contact
Bodies connected have line or point contact
One Body wraps over the other. Eg. Belt wrapping around pulley or chain wrapping around sprocket
OVERVIEW OF KINEMATICS

## Slide 14
Pair | Symbol | Pair Variable | DOF | Relative Motion
Revolute | R |  | 1 | Circular
Prismatic | P |  | 1 | Rectilinear
Screw | H |  | 1 | Helical
Pair | Symbol | Pair Variable | DOF | Relative Motion
Revolute | R |  | 1 | Circular
Prismatic | P |  | 1 | Rectilinear
Screw | H |  | 1 | Helical
REVOLUTE PAIR
PRISMATIC PAIR
SCREW PAIR
LOWER PAIRS
OVERVIEW OF KINEMATICS

## Slide 15
Pair | Symbol | Pair Variable | DOF | Relative Motion
Cylindrical | C |  | 2 | Cylindric
Spherical | S |  | 3 | Spheric
Flat | F |  | 3 | Planar
Pair | Symbol | Pair Variable | DOF | Relative Motion
Cylindrical | C |  | 2 | Cylindric
Spherical | S |  | 3 | Spheric
Flat | F |  | 3 | Planar
CYLINDRICAL PAIR
FLAT PAIR
SPHERICAL PAIR
LOWER PAIRS
OVERVIEW OF KINEMATICS

## Slide 16
MATING GEAR TEETH
CAM-FOLLOWER MECHANISM
Contact between the two bodies takes place only along a line or at a point
HIGHER PAIRS
OVERVIEW OF KINEMATICS

## Slide 17: ANOTHER WAY OF CLASSIFYING KINEMATIC PAIRS
contact between the two bodies at the kinematic pair is maintained by the geometric form
FORM-CLOSED PAIR
FORCE-CLOSED PAIR
Contact needs to be maintained by the application of an external force
OVERVIEW OF KINEMATICS

## Slide 18: MECHANISMS
PLANAR
SPHERICAL
SPATIAL
OVERVIEW OF KINEMATICS

## Slide 19
all the points of the mechanism move in parallel planes
all these parallel planes can be represented by a single plane, (the plane of motion)
A single view perpendicular to this plane of motion reveals the true motion of all the points of a mechanism
PLANAR MECHANISMS
OVERVIEW OF KINEMATICS

## Slide 20: SPHERICAL MECHANISMS
OVERVIEW OF KINEMATICS

## Slide 21
4-R Spatial Linkage
points of all these links move neither in parallel planes nor on the surfaces of spheres, but in 3D space.
they are neither intersecting nor parallel
unlike in a 4R-planar linkage or in a 4R spherical linkage, in this 4R-Spatial linkage, there can be relative motion only for specific dimensions
SPATIAL MECHANISMS
OVERVIEW OF KINEMATICS

## Slide 22
Degree-of-freedom or DOF (denoted by ) of a general mechanical system is defined as the minimum number of independent variables required to describe its configuration completely.
The set of variables (dependent or independent) used to describe a system are termed as the configuration variables. For a mechanism, these can be either Cartesian coordinates of certain points on the mechanism, or the joint angles of the links, or a combination of both.
Set of configuration variables form the configuration space (denoted by ) of the mechanism.
The DOF of a mechanical system may or may not equal the dimension of (denoted by dim()).
Consider a particle free to move in the plane. Clearly, the particle has two DOF, namely: the two independent translations in the plane.
These can be completely described by the Cartesian coordinates or the planar polar coordinates where:
For such a unconstrained system, it is obvious that
But what about Mechanisms ??
DEGREES OF FREEDOM
OVERVIEW OF KINEMATICS

## Slide 23: MECHANISMS TYPICALLY CONSTRAINED
These constraints can be represented as equations in the configuration variables
Independent holonomic constraints
OVERVIEW OF KINEMATICS

## Slide 24
Beginning from just an isolated point to a planar mechanism in a sequence of steps, each step can be analyzed individually
Description of System
Description of the system therefore admits three independent variables.
DOF of planar Mechanisms
OVERVIEW OF KINEMATICS

## Slide 25
A rigid-body confined to a plane has no more degrees-of-freedom than a line embedded in it. In other words, it is enough to specify the coordinates of two points on the body in order to describe its configuration completely.
Introducing third point non-collinear with segment
RIGID BODY IN A PLANE
OVERVIEW OF KINEMATICS

## Slide 26
Consider two freely floating links
It is convenient to think of these DOF as being reflected as the configuration of the lower link, and the relative rotation, of the upper link with respect to the lower one.
creating an open chain of two links
System of links IN A PLANE
OVERVIEW OF KINEMATICS

## Slide 27
Consider that the chain is tethered to a point on the plane.
Additional pair of constraints imposed
WHAT IS THE DOF IN THIS CASE ??
The last pair of constraints essentially kill the translational DOF of the lower link.
Its remaining degree-of-freedom can be conveniently described by the joint angle
OVERVIEW OF KINEMATICS

## Slide 28
N – Total number of links including the fixed link (or base),
J – Total number of joints connecting only two links (if joint connects three links then it must be counted as two joints),
– Degrees of freedom at the joint, and for spatial, for planar manipulators and mechanisms.
Grübler criterion does not work for over-constrained mechanisms (known result from “Mavroidas and Roth(1995), Gan and Pellegrino(2003), review paper by Gogu(2007)).”
PUMA 560 Robot
DEGREES OF FREEDOM
OVERVIEW OF KINEMATICS